## Slide 1
Why SMP Scheduler Scenario Tests
TizenRT PR #7499 · Test code only · Merged to master
BACKGROUND
Dual-core boards show hangs and deadlocks.
Root cause is often the scheduler.
Current tests check APIs only.
A broken scheduler still passes them.
Field hangs are slow and costly to debug.
TODAY vs NEW APPROACH
Today: API tests
Set a value
Read it back
PASS
Passes even if the scheduler is broken.
New: Scenario tests
Apply real load
Observe behavior
PASS / FAIL
Fails when the scheduler misbehaves.
Goal: prove the scheduler behaves correctly under real load.
Notes: Existing kernel tests only confirm that values are stored and returned. They cannot see whether the scheduler actually rotates, preempts or honours affinity. The new scenario tests apply real CPU load and judge the observed behaviour.

## Slide 2
Solution: What We Added
A new test layer on top of the existing kernel. No kernel code changed.
New
Existing
Kernel test runner
Round-robin
2 tests
Starvation
1 test
Priority
4 tests
Affinity
5 tests
Measurement harness
Load, measure, verdict
Starvation monitor
Flags stuck tasks
TizenRT scheduler
Unchanged
CPU 0
CPU 1
DESIGN POINTS
1
Work, not time
Counts work done per task.
2
Per-core counters
No cross-core distortion.
3
Safe cleanup
Tasks stop before any verdict.
4
Opt-in
Off by default. Zero risk.
Notes: Twelve scenarios in four groups share one measurement harness. A background monitor watches for tasks stuck waiting. Everything sits above the kernel; the scheduler itself is untouched.

## Slide 3
How It Works and What It Catches
Real load on real cores. Checks behavior, not return codes.
Create load
CPU-bound tasks
Warm up
200 ms, discarded
Measure
1 to 3 s window
Clean up
Before any verdict
Pass / Fail
Hard + tolerance
WHAT IT CATCHES
1
Round-robin
A task never gets its turn.
2
Starvation
A ready task waits too long.
3
Priority
Urgent work is not preempting.
4
Affinity
A task runs on the wrong CPU.
IMPACT
12
New scheduler checks
0
Kernel code changes
4
Hang/deadlock bug classes
Nightly
Regression, opt-in config
Notes: Each scenario applies a controlled load, discards warm-up, measures, cleans up, then gives a verdict. Impact: early detection of SMP hang and deadlock bugs with zero product risk.